## Slide 1
NPU PLAYGROUND / PROGRESS BRIEF / 09 SEP 2026
Sources: E1 historical experiment; E2 current evaluator validation. Full provenance in notes and evidence.json.
01
From LLM translation
to validated NPU kernels
Agentic feedback improves completion; hardware testing is the next milestone.
01 / TRANSLATION
70% → 95%
Historical task completion
One-shot → agentic
14/20 → 19/20 cases
02 / CORRECTNESS
22/22
Current offline checks pass
Deterministic candidates
264 host input cases
03 / HARDWARE
0 runs
NPU execution blocked
Latency and power
are unmeasured
Different evidence sets: the 22-case evaluator suite is not a rerun of the historical LLM comparison.
Notes: The measured claim is that the evaluated one-shot baseline is unreliable, not that all current LLMs cannot translate NPU code. In the completed historical experiment, baseline completed 14 of 20 kernel-target tasks and agentic completed 19 of 20. AMD completion meant compilation only; Intel completion included historical CPU equivalence and NPU compilation. The newer 22-case suite verifies the upgraded evaluator using deterministic candidates and zero provider calls. It does not demonstrate a new 100% LLM translation rate. No exact NPU binary execution or NPU latency/power measurement is recorded.
Sources:
E1: runs/20260904T011639Z/{experiment.json, metrics.jsonl, summary.json}
E2: runs/container-upgrade-validation/{summary.json, corpus-final/report.json, fixtures/report.json}
E3: docs/validation-results.md and docs/container-simulation-vs-hardware-report.md

## Slide 2
01 / HISTORICAL LLM EXPERIMENT
One-shot translation is not reliable enough
10 kernels × 2 NPU targets; one model call and one compile attempt per task.
Source: E1 • Completed 04 Sep 2026 UTC • Codex CLI 0.144.5 • Model setting recorded as ‘CLI default’.
02
KERNEL
AMD
Intel
CUDA · Reduce sum
PASS
PASS
CUDA · Tiled matrix multiply
PASS
PASS
CUDA · Tiled transpose
PASS
PASS
CUDA · Vector add
FAIL
PASS
HIP · Gamma correction
PASS
PASS
HIP · Image convolution
PASS
FAIL
HIP · Moving average
FAIL
FAIL
Triton · Fused attention
FAIL
PASS
Triton · Fused softmax
PASS
PASS
Triton · Layer normalization
FAIL
PASS
14/20
tasks completed
70% overall completion
6 failures
across both targets
AMD: 4 | Intel: 2
This is one evaluated provider configuration, not a survey of all LLMs.
PASS criteria: AMD = compilation only; Intel = historical CPU equivalence + NPU compilation.
Notes: The table is derived from metrics.jsonl and cross-checked against the completed experiment. AMD baseline passes: reduce sum, tiled matmul, tiled transpose, gamma correction, image convolution, fused softmax (6/10). Intel baseline fails image convolution and moving average (8/10 pass). PASS is historical task completion and must not be described as physical NPU correctness. The provider metadata names codex-cli 0.144.5 with model ‘CLI default’; a precise model version is not pinned in the experiment metadata. This limits broader claims about contemporary LLMs.
Sources:
E1: runs/20260904T011639Z/{experiment.json, metrics.jsonl, summary.json}

## Slide 3
02 / HISTORICAL LLM EXPERIMENT
Agentic feedback recovers 5 of 6 failures
The framework analyzes, generates, compiles and repairs candidates using tool feedback.
Source: E1 • Same 20 kernel-target tasks • Historical acceptance criteria • Search budgets differ.
03
Chart: 
| AMD | Intel
One-shot | 6 | 8
Agentic | 9 | 10
AMD: compilation only | Intel: CPU equivalence + compilation
+25 pp
completion improvement
70% → 95% | 14/20 → 19/20
1 failure remains
AMD fused attention failed the intermediate-representation check.
SEARCH COST Model calls: 20 → 127 Compile attempts: 20 → 216
This shows a benefit from the full agentic workflow; it is not an equal-compute comparison or a 95% device-correctness result.
Notes: The native chart uses final case completion, not the count of successful intermediate compile attempts. Agentic completes 9/10 AMD and 10/10 Intel tasks, compared with baseline 6/10 and 8/10. Five paired baseline failures become agentic successes; AMD fused attention remains unsuccessful with IR mismatch {'output': 0.5390625} after three analysis attempts. Agentic uses 127 provider calls and 216 compile attempts versus 20 and 20 for baseline. Search configuration: three rounds, branching factor three, up to two repair retries per candidate. Therefore the observed +25 percentage points is a workflow result at different budgets, not an isolated causal estimate of agent architecture. Intel host equivalence uses the historical evaluator, not the upgraded independent 12-input suite. AMD historical results contain no source or device correctness proof.
Sources:
E1: runs/20260904T011639Z/{experiment.json, metrics.jsonl, summary.json}

## Slide 4
03 / CURRENT EVALUATOR VALIDATION
The framework now checks correctness explicitly
Independent references, host execution and AMD dataflow checks form the offline acceptance gate.
Sources: E2, E3 • 11 deterministic candidates per target • 12 inputs per candidate • No LLM calls in this suite.
04
01 REFERENCE
Independent expected outputs
→
02 EXECUTE
Candidate source / CPU graph
→
03 CHECK
Numerics + AMD dataflow
→
04 COMPILE
Pinned NPU toolchain
22/22
offline cases pass
11 AMD + 11 Intel candidates
264
host input cases checked
12 inputs × 22 candidates
396
AMD case / schedule checks
132 inputs × 3 schedules
Current validation gate
AMD
Intel
Host output + target compilation
11/11
11/11
FIFO / DMA dataflow simulation
11/11
Not implemented
Faults caught: wrong arithmetic → mismatch | bad DMA stride → bounds error | missing FIFO release → deadlock
These deterministic cases validate the evaluator; the historical LLM experiment has not been rerun under this stricter policy.
Notes: The upgraded suite contains 11 supported static contracts per target: the ten classic manifests plus sigmoid. Each candidate runs on five normal seeds plus seven boundary input families. Across the targets there are 264 host input cases. AMD executes 132 unique dataflow input cases under three schedules, yielding 396 case/schedule comparisons; those are not 396 independent inputs. All 22 deterministic candidate-target cases pass the offline policy; eight additional positive fixtures also pass. Negative checks exercise arithmetic mutation, DMA bounds, missing FIFO release/deadlock and other boundaries. This supports scoped source/graph and modeled-dataflow correctness, not a proof for arbitrary kernels, original CUDA/HIP/Triton execution, or final device binaries. AMD host and dataflow checks share a topology model. The current suite has zero provider calls and is separate from the historical LLM experiment. Current exact-binary target execution remains blocked on both vendors.
Sources:
E2: runs/container-upgrade-validation/{summary.json, corpus-final/report.json, fixtures/report.json}
E3: docs/validation-results.md and docs/container-simulation-vs-hardware-report.md

## Slide 5
04 / AMD AND INTEL SCENARIOS
AMD and Intel validate different representations
Both paths can check supported computations and build target artifacts inside containers.
Sources: E2, E3; P1 AMD dataflow pre-simulation; P2 Intel OpenVINO NPU documentation. Links in notes.
05
AMD
XDNA2 / npu2 / AIE2P
EXECUTES ON HOST
Candidate C++ through audited host support; outputs checked against a reference.
MODELS DATA MOVEMENT
Bounded MLIR FIFO / DMA model checks transfers, bounds and deadlocks.
COMPILES FOR NPU
MLIR-AIE / Peano produce target artifacts, including xclbin and instructions.
Intel
OpenVINO / NPU 4000
EXECUTES ON CPU
Candidate OpenVINO graph runs on the CPU backend; outputs checked against a reference.
CHECKS GRAPH SUPPORT
Offline NPU compilation tests whether the pinned compiler accepts the graph.
COMPILES FOR NPU
The compiler exports an NPU blob. CPU execution does not execute that blob.
Shared gap: 0 exact target-binary executions; all 22 corpus cases report no validated target executor.
Notes: AMD: the upgraded path executes supported candidate C++ through host compatibility support, models emitted MLIR topology and bounded FIFO/DMA behavior, and compiles with the pinned MLIR-AIE/Peano toolchain. Unsupported intrinsics or topology are rejected or marked unsupported rather than treated as verified. This is source/dataflow validation, not an AIE2P instruction-set or cycle-accurate binary simulator. Intel: a candidate graph executes through OpenVINO CPU and also undergoes offline NPU compilation. CPU graph correctness is separate from correctness of the compiled NPU blob. Both profiles have no hardware runner, and every target_execution stage is blocked with NO_VALIDATED_TARGET_EXECUTOR; target-executed validation returns exit code 3. A container can host a real device runner when compatible hardware and drivers are passed through, but these current offline paths do not provide that execution. Vendor documentation is supporting context; the counts and executor status come from local reports.
Sources:
E2: runs/container-upgrade-validation/{summary.json, corpus-final/report.json, fixtures/report.json}
E3: docs/validation-results.md and docs/container-simulation-vs-hardware-report.md
P1: https://xilinx.github.io/mlir-aie/1.4.2/skills/aie-dataflow-presim/SKILL/
P2: https://docs.openvino.ai/2026/openvino-workflow/running-inference/inference-devices-and-modes/npu-device.html

## Slide 6
05 / WHY HARDWARE MATTERS FOR EDGE AI
A correct kernel still needs a hardware benchmark
Edge workloads need acceptable latency and energy use as well as correct outputs.
Sources: E2, E3; P3 MLPerf Tiny (quality, latency, optional energy); P4 MLPerf Edge power methodology.
06
CORRECTNESS
Offline checked
Does it compute the right result?
Source / graph evidence exists.
Exact binary still needs NPU testing.
PERFORMANCE
Unmeasured
Does it meet the response budget?
Measure NPU p50 / p95 latency
and completed work per second.
POWER + ENERGY
Unmeasured
Does it fit the device’s energy budget?
Measure average watts and
millijoules per completed inference.
Container checks cannot establish NPU speed, power or energy per inference.
Measure on AMD and Intel hardware; state whether power covers the NPU, the board or the whole system.
Notes: No NPU latency, throughput, power or energy result is available from the current validation. Missing latency is null, not zero; power and energy were not collected. Functional simulations do not model the device’s actual clock behavior, runtime overhead, memory traffic timing, thermal state or physical power draw with validated accuracy. Hardware measurements should report warmup policy, repeated timings (including p50 and p95), throughput, average power and energy per completed inference. Energy per inference equals measured energy over the measurement window divided by completed inferences. Keep the workload, precision, shape, batch, transfer boundary and measurement boundary explicit. A power rating or CPU runtime is not a substitute for a measured device workload. MLPerf Tiny includes quality, latency and optional energy; MLPerf Edge explains whole-system power measurement. These sources motivate the proposed measurements; our project has no MLPerf submission or performance result.
Sources:
E2: runs/container-upgrade-validation/{summary.json, corpus-final/report.json, fixtures/report.json}
E3: docs/validation-results.md and docs/container-simulation-vs-hardware-report.md
P3: https://mlcommons.org/benchmarks/inference-tiny/
P4: https://mlcommons.org/benchmarks/inference-edge/

## Slide 7
06 / NEXT MILESTONES — PLANNED
Close the loop on real AMD and Intel hardware
The next result should connect translation success, device correctness, latency and energy.
Proposed work based on the gaps in E1–E3. No new hardware or LLM experiments were run to prepare this deck.
07
01
Rerun the translation comparison
Use the upgraded correctness policy for both methods.
Pin the model and compare matched tasks and budgets.
02
Execute the exact target artifacts
Connect each NPU, its drivers and a validated device runner.
Compare device outputs with the same independent references.
03
Measure and optimize for the edge
Collect latency, throughput, watts and energy per inference.
Compare only candidates that pass device correctness checks.
Deliverable: a correctness-filtered latency and energy comparison for both NPU targets.
Notes: These are proposed next steps, not completed work. First rerun the baseline and agentic translation experiment under the new offline acceptance policy, with an explicitly pinned model and a matched-budget comparison in addition to the existing workflow comparison. Second validate a device runner on each target and execute the exact compiled artifacts, verifying outputs before collecting performance. Third benchmark fixed workloads and precision under documented warmup and steady-state conditions, measuring latency, throughput, power and energy. State whether host transfers, loading and compilation are included. A useful result is a set of candidates that preserve device correctness while improving measured latency or energy, with the measurement boundaries disclosed.
Sources:
E1: runs/20260904T011639Z/{experiment.json, metrics.jsonl, summary.json}
E2: runs/container-upgrade-validation/{summary.json, corpus-final/report.json, fixtures/report.json}
E3: docs/validation-results.md and docs/container-simulation-vs-hardware-report.md

## Slide 8
APPENDIX / EVIDENCE AND INTERPRETATION
What the numbers prove — and what remains open
All charts and counts are backed by the saved project reports; source hashes are in evidence.json.
Project: npu-playground • Snapshot prepared 09 Sep 2026 • Speaker notes contain source paths, links and metric definitions.
08
E1 / Historical translation experiment
40 recorded cases: 20 per method
10 kernels × AMD and Intel
Revision: 74f8ae752b23
Codex CLI 0.144.5; model: CLI default
AMD compile-only; Intel CPU + compile
Unequal search budgets
Supports workflow completion, not device correctness.
E2 / Current evaluator validation
22 deterministic candidate-target cases
12 inputs per candidate; 3 AMD schedules
Base: d3efa60a08e5 + working-tree upgrade
0 provider calls; 0 target binary executions
Independent references and negative checks
Not a rerun of the historical LLM experiment
Supports scoped offline checks, not exhaustive proof.
PUBLIC CONTEXT — CLICKABLE SOURCES
P1 AMD dataflow pre-simulation
P2 Intel OpenVINO NPU device
P3 MLPerf Tiny: quality, latency, energy
P4 MLPerf Edge: power measurement
Notes: Evidence snapshot: 2026-09-09. Historical experiment ID 20260904T011639Z completed at 2026-09-04T06:42:44 UTC. The historical revision is 74f8ae752b2396cfb3f5e44226df93f2d8eb277d. The upgraded evaluator was validated on base d3efa60a08e5807c54b40832f3dcb2549f44ea00 plus uncommitted implementation changes. Image identities and compiler fingerprints, original per-case metrics, aggregate counts and SHA-256 hashes of source reports are preserved in the colocated evidence.json. Do not compare 19/20 and 22/22 as a before/after translation accuracy experiment: the candidates, evaluation criteria and use of LLMs differ. The presentation wording intentionally limits the first claim to the measured baseline and limits correctness to the representations actually checked. Full test run before the final alias guard: 98 passed including 23 container tests. Final CPU run: 76 passed, 23 deselected; final boundary checks: 47 passed. The corpus and fixtures were rerun after the guard. Those software checks do not provide hardware performance evidence.
Sources:
E1: runs/20260904T011639Z/{experiment.json, metrics.jsonl, summary.json}
E2: runs/container-upgrade-validation/{summary.json, corpus-final/report.json, fixtures/report.json}
E3: docs/validation-results.md and docs/container-simulation-vs-hardware-report.md
P1: AMD MLIR-AIE dataflow pre-simulation — https://xilinx.github.io/mlir-aie/1.4.2/skills/aie-dataflow-presim/SKILL/
P2: Intel OpenVINO NPU device documentation — https://docs.openvino.ai/2026/openvino-workflow/running-inference/inference-devices-and-modes/npu-device.html
P3: MLPerf Tiny: quality, latency and optional energy — https://mlcommons.org/benchmarks/inference-tiny/
P4: MLPerf Inference Edge: power measurement — https://mlcommons.org/benchmarks/inference-edge/